Addition of Warping Constant and Shape Factor as a Sectional Property for Narrow Parallel Flange (NPB) Sections in IS 12778:2004

Shubham Dashore1, Dolendra Patel2

2Assistant Professor

Shri Shankaracharya Institute of Engineering and Technology , Bhilai, India, 491001

Abstract – Structural steel is an ideal material when it comes to the construction of bridges, buildings and other structures that are large structures. Today, most commercial and industrial buildings are constructed with the help of structural steel. This is a high quality metal which has many industrial uses too. The sectional properties of hot rolled parallel flange steel section includes Moment of Inertia, Radius of Gyration, Elastic Section Modulus and Plastic Section Modulus; each about the major and minor axes. These section properties are commonly required from design point of view. The additional sectional property includes the warping constant and the shape factor which is frequently required while designing by the limit state method.

Keywords – Narrow Parallel Flange Section, Warping Constant, Shape Factor.

INTRODUCTION

Parallel flange sections (Figure 1) are hot rolled steel sections, with parallel flanges having square toes and curves at the root of flange and web. Parallel flange sections are more efficient than the conventional tapered flange sections in terms of strength, workability and economy. Connections are far simpler in parallel flange sections.

Fig.1 Parallel Flange Beams

The Narrow Parallel Flange Sections (NPB) are the type of Indian Standard Parallel Flange Sections in which the nominal flange widths are generally lower than the nominal depth. These sections are designated by nominal depth and nominal flange width and mass of the section in kg/m. For example, NPB 400 x 200 x 67.28 shows the nominal depth as 400 mm, nominal flange width as 200 mm and the mass as 67.28 kg/m.

The compression flange of an beam acts like a column and will buckle side-ways if the beam is not sufficiently stiff or the flange is not restrained laterally. The bending of a beam in the plane of its strong axis, and buckling about its weak axis and accompanied by twisting is characterized as lateral-torsion buckling and the flanges therefore wrap. The warping of beam-flanges is characterized by out-of-plane deformation due to rotation of the beam cross section about the longitudinal axis of the beam. The load at which such a beam buckles can be much less that that causing the full moment capacity to develop. From the elastic stability theory, the expression for the stability limit state, for a steel beam applied with uniform moment, the critical moment Mcr is given by:-

where, EIy = flexural rigidity (minor axis)

GIt = torsional rigidity

It, Iw = torsion constant and warping constant.

L = unbraced length of the beam subjected to  constant moment in the plane.

The equation for calculating the elastic critical moment corresponding to lateral torsional buckling of a doubly symmetric torsionally restrained prismatic beam subjected to uniform moment in the unsupported length is given by equation :-

where, Iy, Iw, It = moment of inertia about the minor axis, warping constant and torsional constant, respectively.

G = modulus of rigidity

LLT = effective length against lateral-torsional      buckling

For a ductile material like structural steel, a member reaching yield at the extreme fibers retain a reserve of strength that varies with the shape factor. Higher the shape factor, more ductile will be the section and will give greater deflection at collapse. This implies that such a section gives longer warning before collapse. In other words, shape factor gives an indication of reserve capacity of a section from onset of yielding at extreme fibers to full plastification. Shape factor may be defined as the ratio of the plastic moment and the yield moment of the section. It is a function of cross section form or shape.

METHOLOGY

Lateral torsional buckling is a potentially more significant design consideration for the beam section which is much less stiff laterally. The computation of these constants is often necessary for computing the elastic critical moment corresponding to lateral torsional buckling of a doubly symmetric prismatic beam subjected to uniform moment in the unsupported length and torsionally restraining lateral supports. This is given by the following expression in Draft IS 800 :-

This expression for the elastic critical moment for the basic problem clearly demonstrates the influence of moment of inertia about the minor axis (Iy), torsional and warping constants (It and Iw respectively) of the cross section; it also demonstrates the importance of unsupported length of the beam.

Warping constant is given as:-

Fillets are generally neglected while computing the warping constant. This has a very little effect upon the values of warping constant. The above expression can be written as:-

where, tf = thickness of the flange.

bf= width of the flange.

D = overall depth of the section

As the shape factor varies with the reserved strength of the structural steel giving an idea of the ductility of the section, it can be given by :-

Shape Factor (S) =

The Elastic section modulus Ze is defined as the first moment of area and is expressed as I/y, where I is the moment of inertia of the section and y is the distance of the extreme fibre distance from the neutral axis whereas plastic section modulus is the combined statical moment of the cross-sectional area above and below the equal area axis of a completely yielded section.

CONCLUSION

These sections are economical and more efficient as compared to conventional tapered sections. The uses of NPB sections were not very common in India, until few years before, due to non-availability of the same in medium in large sizes. Such sections are now being produced in India and are expected that use of such sections will increase in few years ahead.

The addition of such sectional properties of the NPB sections helps to reduce the work time and its addition in the IS code will make it more easier for the practicing designers and budding engineers for designing purposes as the values will be readily available for them.

The shape factor of all the NPB sections generally lies in the range of 1.0 to 1.25. This means that even when the extreme fibers has yielded, it can take up to 25% more moment than the applied one before it gives up for good.

REFERENCES

- Draft IS 800, “Code of Practice for General Construction in Steel (Third Revision)”, Bureau of Indian Standards, New Delhi, India, October 2004.

- N. Subramanium, “Design of Steel Structures – Limit State Method”, ”Oxford publication”,2018

- IS 12778 : 2004, “Hot Rolled Parallel flange Steel sections for Beams, Columns, and Bearing Piles – Dimensions and Section Properties (First revision)”, Bureau of Indian Standards, New Delhi, September 2004.

- S.S. Bhavikatti, “Design of Steel Structure”, by Limit State Method as per IS 800:2007, Fifth Edition, September 2017.

- IS 2062 : 1999, “Steel for General Structural Purposes”, Bureau of Indian Standards, New Delhi, India.

- IS 800 : 1984, “Code of Practice for General Construction in Steel (Second Revision)”, Bureau of Indian Standards, New Delhi, India.

- IS 8500 : 1991, “Structural Steel – Micro alloyed (Medium and High Strength Qualities)”, Bureau of Indian Standards, New Delhi, India.

- S.K. Duggal, “Limit State Design of Steel Structures”, Second Edition, Tata McGraw Hill Publication, 2014.

- Seaburg, P.A., and Carter, C. J., “Torsional Analysis of Structural Steel Members”, Steel Design Guide Series No. 9, Second Printing, American Institute of Steel Construction, Chicago, Illinois, October 2003.

- SteelUK - Dimensions and Properties of UK structural Steel shapes, Techno Consultants Ltd., Manchester, England, November 2000.

- Himanshu Gaur, “Optimization of Sectional Dimensions of I-Section Flange Beams and Recommendations for IS 808: 1989”,  Kota, India, 31st March 2016.

- Keith M. Mueller, “Torsional Analysis of Steel Sections”, American Institute of Steel Construction, Chicago, 2002.

Table 1: Additional Sectional Properties of Narrow Parallel Flange (NPB) Sections

Table 1 (Continued): Additional Sectional Properties of Narrow Parallel Flange (NPB) Sections

Table 1 (Continued) : Additional Sectional Properties of Narrow Parallel Flange (NPB) Sections

Table 1 (Continued) : Additional Sectional Properties of Narrow Parallel Flange (NPB) Sections