Heat Transfer Performance Analysis of Water Nano Particles Combination for Corrugated Plate Heat Exchanger

Prof. Mahesh Chandrabhan Shinde1

1Assistant Professor

SRTTC Faculty of Engineering, VIT Campus Kamshet, Pune, India,410 405

Abstract: In a conventional plate heat exchanger, increase in heat transfer area directly affects the size of heat exchanger by making it bulky. To overcome this limitation and to test the capability of compact heat exchanger namely corrugated plate heat exchanger, there is a need to increase the heat transfer coefficient of the base fluid. Preferably, addition of Nano particles along with the provision of corrugations on the plates will lead to an increase in effectiveness of the heat exchanger. This study is carried to enhance heat transfer of water by addition of Nano fluids and test the test rig for parallel flow arrangement and counter flow arrangement for different mass flow rates of hot fluid. design of heat exchanger is done based on sizing, that is determination of heat transfer parameters, number of thermal plates required and physical dimensions. It is observed that there is a slight drop in effectiveness with increase in heat capacity ratio. For water as a working fluid the value of effectiveness varies from 0.66 to 0.80 while that of for Nano fluids the value of effectiveness varies from 0.70 to 0.82.

Keywords Corrugated PHE, Counterflow, Effectiveness, Nano Fluids, Sizing etc. Corrugated PHE, Counterflow, Effectiveness, Nano Fluids, Sizing etc.

INTRODUCTION

Plate heat exchanger (PHE) originally received particular attention from the dairy industry due to their suitability in hygienic application. Soon their use became wide spread in the food, juice, beverage and pharmaceutical industries due to the ease of cleaning and the thermal control required for sterilization and pasteurization Heat exchangers are devices that facilitate the exchange of heat between two fluids that are at different temperature while keeping them without mixing with each other. These exchangers are classified according to construction, flow arrangement; number of fluids, compactness, etc. The use of heat exchanger gives higher thermal efficiency to the system. In many applications like power plants, petrochemical industries, air conditioning etc. heat exchangers are used. Plate heat exchanger is generally used in dairy industry due to its ease of cleaning and thermal control. The plate heat exchangers are built of thin metal heat transfer plates and pipe work is used to carry streams of fluid. Plate heat exchangers are widely used in liquid to liquid heat transfer and not suitable for gas to gas heat transfer due to high pressure drop. The flow of heat in a process can be calculated as, Q=hA∆T where , Q  is to heat flow, h is heat transfer coefficient, A is the heat transfer area, ∆T is the temperature difference that results in heat flow. It can be stated from this equation that increased heat transfer can be achieved by: increasing ∆T, increasing A, increasing h. A greater temperature difference ∆T can lead to increase the heat flow but ∆T is often limited by process or material constraints. Maximizing the heat transfer area (A) leading to increase in the size of heat exchanger which ultimately leads to unwanted increase in weight and cost. And Heat transfer enhancement can also be achieved by increasing the heat transfer coefficient h either by using more efficient heat transfer methods, or by improving the transport properties of the heat transfer material. So in order to overcome above problems, addition of Nano-particles in the base fluid is recommended for the purpose of improving heat transfer.

METHOLOGY

Table 1: Thermo Physical properties of fluid

| Property | Unit (metric) | Hot water (mean temp) | Cold water (mean temp) |
| --- | --- | --- | --- |
| Heat capacity(Cp) | J/kgK | 4197 | 4178 |
| Thermal conductivity(k) | W/mK | 0. 668 | 0. 6316 |
| Dynamic viscosity (μ) | Ns/m2 | 0. 000378 | 0.000370 |
| Density (ρ) | Kg/m3 | 974.851 | 994.034 |

Fig. 1- Experimental Setup

Experimental setup consists of tanks, pumps, Rotameter, U tube manometer, temperature indicators, corrugated plate heat exchanger. test the performance of heat exchanger for parallel and counter flow arrangement with water as a working fluid. The heat exchanger has total 13 plates and it is constructed using Stainless Steel AISI 316. Each plate is flat and has thickness of 0.5 mm. The total heat transfer area is 0.2548 m2. Thermometers are placed to measure inlet and outlet temperatures of hot and cold water. following trials are taken 	                             1. Test on corrugated plate heat exchanger with parallel flow arrangement (with water) 		            	                   2. Test on corrugated plate heat exchanger with counter flow arrangement (with water)	         		         3. Test on corrugated plate heat exchanger with parallel flow arrangement (with water and Nano-fluids) 	   4. Test on corrugated plate heat exchanger with counter flow arrangement (with water and Nano-fluids)

DESIGN

2.1 Heat duty (Q):

Heat rejected by hot water,

𝑄= 𝑚ℎ𝐶𝑝ℎΔ𝑇ℎ …….………………………… (2. 1)

𝑄= 𝑚ℎ𝐶𝑝ℎ(𝑇ℎ1−𝑇ℎ2)

=0.25×4194× (85−65)

Q =20970𝑊

Where, mh =mass flow rate of hot water in Kg/s,

Cph=specific heat capacity of hot water J/Kg K

ΔTh = temperature difference between inlet and outlet of hot water in K

Heat absorbed by cold water,

𝑄 = 𝑚𝑐𝐶𝑝𝑐Δ𝑇𝑐 ………………………………. (2. 2)

= 𝑚𝑐𝐶𝑝𝑐 (𝑇𝑐2− 𝑇𝑐1) 20970

=0.25×4178× (𝑇𝑐2− 25) 𝑇𝑐2

= 45.070𝐶

Where, mc =mass flow rate of cold water in Kg/s,

Cpc= specific heat capacity of hot water in J/Kg K

ΔTc=temperature difference between inlet and outlet of cold water in K

2.2 Thermo physical properties at fluid mean temperature:

1. Hot water mean temp = (85+65)/2 = 75 0𝐶

2. Cold water mean temp = (25+45.07)/2 = 35.03 0𝐶

2.3 The hydraulic diameter:

𝐷𝑒=2𝑏/𝜓

=2×0.00224 / 1.16

𝐷𝑒 = 0.00386 m

The flow area for water:

𝐴=𝑁𝑊𝑏…… ………………. (2.3)

Where,

A= flow area for water in m2, N=number of water chambers

W =width of plate in m b =distance between two plates in m

2.3.1 For hot water

𝐴ℎ = 𝑁ℎ𝑊𝑏 …… …………. (2.4)

Here,

Nh= 6, W=0.090 m, b =0.00224 m

𝐴ℎ=6×0.0.090×0.00224

𝐴ℎ=0.0012 𝑚2

2.3.2 For cold water					       𝐴𝑐 = 𝑁𝑐𝑊𝑏……       …………… (2.5)

Here,

Nh= 7, W=0.090 m, b =0.00224 m 					Ac=7×0.090×0.00224

𝐴𝑐=0.001411 𝑚2

2.4 Velocity of water:											𝑉= 𝑚÷ (𝐴 ⍴) …………………………(2.6)

Where

V= velocity of hot water in m/s, m=mass flow rate in Kg/s

A= flow area for water in m2, ρ = density of water in Kg/m3

2.4.1 For hot water

𝑉ℎ= 𝑚ℎ𝐴ℎ𝜌ℎ.………………. (2.7)

Here,

mh=0.25 Kg/s, Ah =0.0012 m2, ρh =974.851 Kg/m3

=0.25/ (974.851×0.0012)

𝑉ℎ =0.02137 𝑚/𝑠

2.4.2 For cold water

𝑉𝑐 = 𝑚𝑐𝐴𝑐𝜌𝑐…………………(2.8)

Here,

mc=0.25 Kg/s, Ac =0.001411 m2, ρc = 994.034 Kg/m3

=0.250.001411×994.11

=0.1783 𝑚/𝑠

2.5 Reynolds number

2.5.1 For hot water:

𝑅𝑒ℎ= 𝜌ℎ𝑉ℎ𝐷𝑒/μℎ            ………… …… (2.9)

Here,

ρh = 973.851 Kg/ m3, Vth = 0.2137 m/s, De= 0.00386 m, μh = 0.000378 Ns/m2

= (973.851× 02137× 0.00386)/0.000378

𝑅𝑒ℎ=2127.34

2.5.2 For cold water:

𝑅𝑒𝑐= 𝜌𝑐𝑉𝑐𝐷𝑐/μ𝑐...……………………. (2.10)

Here,

ρc = 993.034 Kg/ m3, Vc = 0.1783 m/s, De = 0.00386 m

μh = 0.000720 Ns/m2                                                      	 = (993.034× 0.1783× 0.00386)/0.000720

𝑅𝑒𝑐 =950.18

2.6 Prandtl number

2.6.1 For hot water,

𝑃𝑟ℎ = μℎ𝐶𝑝ℎ/𝑘ℎ   …………………… (2.11)

Here,

μh= 0.000378 Ns/m2, Cph= 4194 J/Kg K, kh =0.668 W/mK

= (4194×0.000378)/0.668

𝑃𝑟ℎ=2.3732

2.6.2 For cold water, 											𝑃𝑟𝑐 =μ𝑐𝐶𝑝𝑐/𝑘                  …………. (2.12)

Here,

μc= 0.000720 Ns/m2, Cpc= 4178 J/Kg K

kc =0.6316 W/mK

=4178×0.0007200.6316

𝑃𝑟ℎ=4.7627

2.7 Nusselt Number

Here Re < 2000 so taking relation for laminar flow,

𝑁𝑢 = 0.662 𝑅𝑒0.5𝑃𝑟0.33………………. (2.13)

2.7.1 For hot water

𝑁𝑢ℎ = 0.662 𝑅𝑒ℎ0.5…………………. (2.14)

Convective heat transfer coefficient for hot water (hh):

ℎℎ = (0.662) (𝑘ℎ/𝐷𝑒) 𝑅𝑒ℎ0.5𝑃𝑟ℎ0.33

Here,

kh=0.668W/mK, Reh=2127.32, Prh=2.3732 		   =0.662× (0.668/0.00386) × (2127.32)0.5× (2.3732)0.33

ℎℎ=7027.90𝑊/𝑚2. 𝐾

Where,

hh is the hot fluid heat transfer coefficient

2.7.2 For cold water											 𝑁𝑢𝑐 = 0.662 𝑅𝑒𝑐0.5𝑃𝑟𝑐0.33   …………. (2.15)

Convective heat transfer coefficient (hc):

ℎ𝑐 = (0.662) 𝑘𝑐/𝐷𝑒) 𝑅𝑒𝑐0.5𝑃𝑟𝑐0.33…              …... (2.16)	        = (0.662) × (0.6316/0.00386) × (950.18)0.5× (4.7627)0.33

ℎ𝑐=5588.65𝑊/𝑚2𝐾

Where, hc is the cold fluid heat transfer coefficient

2.8 Overall heat transfer co efficient:

The overall heat transfer coefficient for a clean surface is given by

1/𝑈=1/ℎℎ+𝑡/𝑘𝑝+1/ℎ𝑐………………… (2.17)

Here,

hh =7027.90 W/m2. K, hc = 5588.90 W/m2. K

Kp = 17.5 W/m2K        t = 0.0005m

= (1/7027.90) +(0.0005/17.5) +(1/5588.90)

1/𝑈= 0.0003497

𝑈 = 2858.81𝑊/𝑚2. 𝐾

2.9 Logarithmic Mean Temperature Difference (LMTD):

𝛩𝑚 =[[(𝑇ℎ1−𝑇𝑐2) −(𝑇ℎ2−𝑇𝑐2)] / 𝑙𝑛[(𝑇ℎ1−𝑇𝑐2)/(𝑇ℎ2−𝑇𝑐2)]] ………………………………………………. (2.18)

= [[(85−45.07) −(65−45.07)]/ 𝑙𝑛 [85−45.0765−45.07]]

𝛩𝑚= 28.78 0C

2.10 Area required

𝑄=𝑈𝐴𝛩𝑚…         ……………..…….… (2.19)

20970=2858.81×𝐴×28.78.78

𝐴= (20970 / 2858.81×28.78)

𝐴=0.2548 𝑚2

Area for single plate = 0.231×0.090=0.020𝑚2

Total no of plates = 𝑇𝑜𝑡𝑎𝑙 𝑎𝑟𝑒𝑎 / 𝐴𝑟𝑒𝑎 𝑜𝑓 𝑠𝑖𝑛𝑔𝑙𝑒 𝑝𝑙𝑎𝑡𝑒

= 0.2548 / 0.020

= 13

In this design total area of heat transfer obtained is 0.2548𝑚2 and total numbers of plates required are 13.

CONCLUSION

Fig.02 Comparison of effectiveness for water and Nano fluids

The main focus of this project is to understand the effect of nanoparticles when added with working medium and to investigate experimentally its effect on various performance parameters of PHE. The following are the findings of this experimental investigation:		   1. Convective heat transfer coefficient increases with Reynolds number and mass flow rate for both parallel and counter flow arrangement. This is due to the fact that flow becomes more turbulent and cause for turbulence can be attributed to plate geometry i.e., corrugations as well as high flow velocity.		                                2. Maximum temperature drop achieved for this heat exchanger is in the range of 240C – 270C, which is comparatively higher. This can be attributed to enhanced thermos physical properties as well as plate geometry.

ACKNOWLEDGMENT

It gives me immense pleasure to express my profound thanks to all those people who have taken a great deal of interest and contributed plenty of their help in my work.

|  | Prof. Mahesh Chandrabhan Shinde Assistant Professor ME (Heat Power Engineering) Mechanical Engineering Department VIT Campus Kamshet Pune |
| --- | --- |

REFERENCES

[1] R. K. Shah and D. P. Sekulic, (2003). “A Textbook of Fundamentals of Heat exchanger design”

[2] R. K. Shah and S. G. Kandilkar MAY (1989) “Multipass Plate Heat Exchangers- Effectiveness-NTU Results and Guidelines for Selecting Pass Arrangements”, Transactions of ASME, Vol.111,

[3] R. Saidur, S.N. Kazi, M.S. Hossain (2011) “A review on the performance of nanoparticles suspended with refrigerants and lubricating oils in refrigeration system”

[4] R. Saidur, K.Y. Leong, H.A. Mohammad (2011) “A review on applications and challenges of nanofluids”, Renewable and Sustainable Energy Reviews, 1646–1668

[5] Jogi Nikhil G., Lawankar Shailendra M. Oct (2012) “Heat Transfer Analysis of Corrugated Plate Heat Exchanger of Different Plate Geometry”, International Journal of Emerging Technology and Advanced Engineering, ISSN 2250-2459, Volume 2,

[6] Murugesan M.P. and Balasubramani R. February (2013), “The Experimental Study on Enhanced Heat Transfer Performance in Plate Type Heat Exchanger” Research Journal of Engineering Sciences, Vol.2(2),16-22, ISSN 2278-9472.

[7] Vishal R. Naik, V.K. Matawala (April 2013) “Experimental Investigation of single phase Chevron Type Gasket Plate Heat Exchanger”, International Journal of Engineering and Advanced Technology(IJEAT), ISSN: 2249-8958, Volume-2, Issue-4,

[8] T K S Sai Krishna, S G Rajasekhar, C Pravarakhya July-August (2013) “Design and Analysis of Plate Heat Exchanger with CO2 and R134a as working fluids”, International Journal of Mechanical Engineering and Technology (IJMET), ISSN 0976-6359 Volume 4. Issue 4

[9] Masoud Asadi, Ramin Haghighi Khoshkhoo (February 2014) “Effects of Chevron Angle on Thermal Performance of Corrugated Plate Heat Exchanger”, International Journal of Engineering Practical Research (IJEPR) Volume 3 Issue 1,

[10] Raman Chouda (September 2014) “Analysis of Heat Exchanger with Nano fluids”, International Journal of Core Engineering & Management (IJCEM) Volume 1, Issue 6,