“EVALUATION OF PART PRODUCTION METHODOLOGY IN AUTOMOTIVE INDUSTRY.”

Suryakant Namdeo Wahane1, Dr Achal Shahare2,

1M.tech student , Department of Mechanical Engineering

G.H Raisoni Academy of Engineering &Technology , NAGPUR , INDIA, 440016

2Assisant Professor , Department  of Mechanical Engineering

G.H Raisoni Academy of Engineering &Technology , NAGPUR , INDIA, 440016

Abstract –Methods of Production, Planning & Inventory Control, Industrial Layout, and Statistical Quality Control of component in Industry gives new era for production of defect free components. When creating the design solutions the following challenges arose: failure in function, costumer complaints, limited space in production floor, implementing without impacting the production process or the associate’s tasks, upholding the company’s ethics code and creating solutions compatible with the company’s technology. For better process performance each component would be assigned a bin in the production line, and the material handler would be in charge of loading the components into the bins and need to have proper design analysis (DA).

This resulted less material on the production floor, better utilization of the company’s transportation trucks, and more efficient material flow since smaller batches are easier to control and transport within the facility. This resulted in a simpler, more intuitive database which will facilitate the data recollection process and a better record for scrap/reworked materials. This project, Freight Data Analysis, creating a detailed freight database so all the data could be found in a single place and creating a Standard Operating Procedure (SOP). Both of these solutions were aimed towards creating a better record and control for the freight expenses. With more detailed and accessible records it will be easier to identify opportunities to reduce costs and control freight expenses; it will guarantee that all expenses regarding fright are thoroughlyexamined before being approved in fabrication and assembling of different components etc

.

Keywords- Production methodology of part production and failure analysis.

Failure/performance evaluation with case study:

Problem selection matrix:

Problem definition : Metal Chips in Threading of Top Link Spindle (Tls)  During  Threadrolling Operation On Thread Rolling Machine  Rt-02

Current Status  of the Problem / Issue (Quantified) : From last 2 month there is no part  found  having  metal chips on threading

Improvement Target (Quantified):  Reducing the production loss and zero rejection / rework.

1.Benefits projected / Impact of Project: Saving production loss.

2.  Customer satisfaction

Chapter 5:

Failure / performance evaluation:

5.1   : Select the Theme

- Problem Selected: Metal chips found in treading of Top Link Spindle during thread rolling on thread roll machine RT-02

Line Rejection  :

| Month | Production | Line Rejected for Threading Chips |
| --- | --- | --- |
| Aug-17 | 10559 | 379 |
| Sep-17 | 15450 | 547 |
| Oct-17 | 6021 | 218 |
| Nov-17 | 13492 | 628 |

Rework done  by  Hand  die pass  and  remove chips  in thread

5.2. Justify the Choice

5.2..1 History of the Problem

07 No. TLS was rejected on 05/10/2017

21 No. TLS was rejected on 06/12/2017

5.2.2  Containment action taken (Immediate Correction) to Protect Customer:

Segregation & Rework of parts done at customer  Plant by extra manual on contract ,sent two Quality person for segregation & Reworked  of 3000 No. parts  so that the production will not get affected till permanent solution through this project is institutionalized.

5.3  Understand Current Situation:

5.3.1 Understand & Mention Present Process Controls through

- Recommended actions specified in FMEA/QCPC for the problem selected.

- Action taken on past complaints.

5.3.2 Observation  of the Process:

Threading Operation Photo

5.3.3 Observation  of the Process

Process Flow  Diagram

5.3.4 Observation  of Symptoms:

- Burrs / Chips in threads

- Thread go gauge not enter in thread ¾” x16 unf-2A due to burr’s in thread.

- Fitment problem during assembly.

5.3.5 : Observation of Variation:

For the brainstorming session all the members of our  team were present. We Identified  various suspected source of variation for chip formation in thread during thread rolling and we identified  38 source of variation  during brain storming session by the team.  Following are SSV

- Hydraulic Pressure Excess

- Hydraulic Pressure Low

- Blade height less or more

- Improper Machine Setting

- Rolling Time not set properly

- Unskilled operator

- Unbalancing part during operation

- Machine slide loose / gap

- Thread Roll damage

- Material soft

- Roller diameter undersize

- Thread Height less

- Roll matching setting not ok

- Variation in OD of Bar

- Dusty / Dirty / Metal  chips in cutting oil

- Effective dia. Oversize

- Loose chips in antirust oil at final stage

- Wire brush cleaning not done

- Improper supply of cutting oil

- Cutting oil not as per required  specification

- Guide blade not set

- Center height  of roll wheel not set

- Center height of part not set

- Wire wheel not clean well

- Cleaning wire wheel dirty / metal chip

5.4 ANALYSIS

5.4.1 : Possible Causes:

Brainstorming- Total 21 possible cause were generated during Brian storming session

- Cutting oil not  as per Specification

- Hydraulic Pressure variation

- Blade height variation

- Machine slide loose / gap between slide

- Rolling Time not set properly

- Unskilled operator

- Unbalancing part during operation

- Thread Roll damage

- Material soft

- Roller diameter  undersize

- Thread Height less

- Roll matching setting not ok

- Metal chips in  Cutting Oil

- Effective dia. Oversize

- Loose chips in antirust oil at final stage

- Wire brush cleaning not done.

5.4.2 Cause and Effect Diagram:

5.4.3 Probable Causes:

- Machine slide Loose

- Unskilled operator

- Material Soft

- Metal chips in  Cutting Oil

- Roll matching setting not ok

- Blade height variation

- Thread Roll damage

- Effective dia. Oversize

5.4.4 Testing of Hypothesis:

| Sr. No. | Probable Root Cause | Method of Testing | Observation | Result (Valid / Invalid) |
| --- | --- | --- | --- | --- |
| 1 | Machine Slide loose | Dial Indicator | On full Load Thread roll was getting deflected by 1 mm against 0.2 mm | Valid |
| 2 | Thread roll Machining | Checked on trial piece & no mismatch found on thread impression is observed | Checked on trial piece & no mismatch found on thread impression is observed | Invalid |
| 3 | Hyd. Pressure variation | On Pressure Gauge | Pressure observed < 15 ton | Invalid |
| 4 | Center height of part variation | 50 parts lot check height by dial on machine | Observed variation on height 0.1 to 0.08 mm | Valid |
| 5 | Guide Blade height variation | Checking by vernier caliper | Observed as per required | Invalid |
| 6 | Unskilled Operator | Selection of Operator as per skill matrix | Skilled operator was used | Invalid |
| 7 | Metal chips in Cutting Oil | Filter and separator | Fine chips found in oil | Valid |
| 8 | Material Soft | Hardness tester | As per material specification | Invalid |
| 9 | Thread Roll damage | Visual checking | Observed no damage | Invalid |
| 10 | Effective dia. Oversize | Increase the diameter of Part | Observed Chips formation in thread | Valid |

5.4.5 Possible Root  Cause:

- Machine Slide loose

- Center height of part variation

- Metal chips in  Cutting Oil

- Effective dia. Oversize

| Sr. No. | Dia. Of Part | Observation of Chips in thread |
| --- | --- | --- |
| 1 | 17.900 mm | OK |
| 2 | 17.905 mm | OK |
| 3 | 17.910 mm | OK |
| 4 | 17.915 mm | OK |
| 5 | 17.920 mm | OK |
| 6 | 17.925 mm | OK |
| 7 | 17.930 mm | OK |
| 8 | 17.935 mm | OK |
| 9 | 17.940 mm | OK |
| 10 | 17.945 mm | Not OK |
| 11 | 17.950 mm | Not OK |
| 12 | 17.955 mm | Not OK |
| 13 | 17.960 mm | Not OK |
| 14 | 17.965 mm | Not OK |
| 15 | 17.970 mm | Not OK |

5.4.6:  Final Validated Root Causes

- Center height of part variation

- Effective dia. Oversize

- Metal chips in  Cutting Oil

- Machine Slide Loose

5.4.7:Why –Why analysis for arriving at the possible solution :

| Sr. No. | ROOT CAUSES | WHY? | WHY? | WHY? |
| --- | --- | --- | --- | --- |
| 1 | Machine Slide loose | Gap Between Slide | Slide Worn Out | Scarping Not Done |
| 2 | Center height of part variation | Part diameter vary | Tolerance very wide |  |
| 3 | Metal chips in Cutting Oil | Oil not filter | No metal separator |  |

5.4.8:  Implementation Plan for the Remedies developed:

| Sr. No. | List of Root Causes | Remedial Action |
| --- | --- | --- |
| 1 | Machine Slide loose | Machine Slide scraping |
| 2 | Part Diameter over size | Machining Tolerance Change +/- 0.1 to +/- 0.05 mm |
| 3 | Metal chips in Cutting Oil | Magnetic Separator place into Oil tank |

5.4.9: Confirm the Effects:

| Month | Production | Line Rejection |
| --- | --- | --- |
| Feb-18 | 12481 | 8 |
| Mar-18 | 10897 | 0 |

Intangible Benefits:

Line Rejection of  TLS  chips in Threading on Thread Roll was reduced 90 %  in month of January  2018  and  Zero line rejection in month of February 2018. We are observing  continuously  there is not found the chips in thread .

  - STANDARDIZATION:

5.5.1  List of Documents changed :

These are Document are at thread rolling of TLS were Updated

- Control Plan

- SOP

- Process Diagram

5.5.2 Horizontal Deployment:

We have Planned  to Implement  same control on  other thread rolling machine  and part having  Thread rolling.

5.5.3 : Training given to concerned people

Operator  at thread  rolling  operation and  Supervisor   were given training about new  SOP, Control Plan and Other related document.

5.5.4 Additional audit checks introduced for:

Line Inspector and final inspection 100% visually inspected.

CONCLUSION

The evaluation of part production methodology helpful to optimize use of resources, equipments and manpower. Somehow help to reduce total time cycle for part production.

It can be utilize to improve new techniques for process qualification and capability of part production studies. Now a days the statically quality control plays vital role in 7 qc tools for problem solving.

This project summaries part production methodology and  the possible causes in threading spatter problem. Meanwhile it is associated with all similar problem arose. The customer may benefit with such studies taken in-house defect before dispatch lead customer satisfaction.

FUTURE SCOPE

- Part production with scheduling Process flow diagram, control plan and failure mode effect analysis.

- Improvement in conventional production techniques with statistics.

- Design analysis and reduce future failure

- To reduce the overall cost of manufacturing and to make it Economic.

- To reduce wastage of time (time required for repairing and re-manufacturing)

- To achieve production in time

- To reduce work in inspection department

REFERENCES

    - Int. J. Industrial and Systems Engineering, Vol. 1, No. 4, 2006 by Kanthi M.N. Muthiah* and Samuel H. Huang

    - Carrie, A. and Macintosh, R. (1997) ‘An assessment of GRAI grids and their use in the strathclyde integration method’, Production Planning and Control, Vol. 8, pp.106–113

    - Feigenbaum, A.V. (1991) Total Quality Control, New York: McGraw Hill

    - B. Agard and A. Kusiak, Standardization of Components, Products and Processes with Data Mining,International Conference on Production Research Americas 2004, Santiago, Chile, August 1-4, 2004.

# Application of Statistical Process Control (SPC) in Manufacturing Industry in a Developing CountryIgnatio Madanhire

    - Research on the Use of Statistical Methods in Quality Control in Selected Czech Manufacturing Companies by  MARTIN KOVÁŘÍK, PETR KLÍMEK

    - Success factors in the implementation of statistical process control: action research in a chemical plant by Jose Carlos de Toledoa *, FabianeLetíciaLizarellia , ManoelBispo Santana Juniora

.