Multi Attribute Decision Making In Optimization of Corrugated Sheet Box Industry

Prof.S.R.Jachak1, Miss.Aditi Taley2

jachak_shrikant@yahoo.co.in1    adititaley09@gmail.com2

1(Assistant Professor,/Department of Mechanical Engineering/Yeshwantrao Chavan College of Engineering/RTMNU, Nagpur)

2(M-tech Student/Department of Mechanical Engineering/Yeshwantrao Chavan College of    Engineering/RTMNU, Nagpur)

Abstract – The aim of this research work paper is an optimization of corrugated sheet box industries by using 15 common attributes from three different industries by using MADM methods like AHP, TOPSIS & PROMETHREE so that we can find out best alternative.

Systematic decision-making analysis can help decision maker to summarize and judge all information effectively and to define right question and to find out optimum and the most appropriate solution.  Analytic hierarchy process(AHP) is a structured technique for organising and analysing the complex decisions. TOPSIS is also one of the MADM method, in this technique two artificial alternatives are hypothesized. Positive ideal alternative which corresponds to the maximum value and negative ideal alternative which corresponds to the minimum value. PROMETHREE offers complete ranking from the best alternative to the worst one. In this method pair of alternative is compared.

From this investigation , it is found that ,these technique like AHP and PROMETHREE  will not only help the researcher in providing the matter concerned but also helps to understand the optimization problem in better way with possible solution.

Keywords-Multi Attribute decision Making, Analytic Hieryachi Process (Ahp)

INTRODUCTION

Multi-attribute decision making method, which was taking as the base for the decision making model, is one of the decision-making support methods. The MADM theory offers a formal base for the establishment of a model, in which the key criteria is interconnectedness of assessments according to the individual parameters that result in an integrated assessment.

Engineers are always making design decisions, whether it's the design of a thermal fin or the location of a new manufacturing plant. Poor decisions could result in the loss of money, resources, and time. Therefore, it is important that engineers make logical and well reasoned decisions. Systematic decision-making analysis can help decision maker to summarize and judge all information effectively and to define right question and to find out optimum and the most appropriate solution.

Analytic hierarchy process(AHP) is a structured technique for organizing and analyzing the complex decisions. TOPSIS is also one of the MADM method, in this technique two artificial alternatives are hypothesized. Positive ideal alternative which corresponds to the maximum value and negative ideal alternative which corresponds to the minimum value.  PROMETHREE offers complete ranking from the best alternative to the worst one. In this method pair of alternative is compared.

From this investigation, it is found that ,these technique like AHP and PROMETHREE  will not only help the researcher in providing the matter concerned but also helps to understand the optimization problem in better way with possible solution. The purpose for using utility  theory in decision making is to create a mathematical model to aid the process. It gives the decision maker the ability to quantify the desirability of certain alternatives. Utility theory is for design scenarios where uncertainty and risk are considered. The end result of using this method is a function which represents the designer's preferences, given a certain set of design attributes.

INDUSTRIAL SURVEY

Name of Industries are given below:

1] Sunpack Industries Private  Ltd, N-45 , MIDC Badnera Road, Amravati

2] Shrinath Packers Pvt. Ltd , C- 40, MIDC Badnera Road, Amravati

3] Mahalakxmi packers  Private Ltd , MIDC , Amravati

Fig. Packing Boxes

CORRUGATED SHEET BOX PRODUCTION PROCESS

There are mainly six workstation

1] Corrugation

2] Pasting

3] Printing

4] Creasing.

5] Slotting

6] Stitching & Punching

Fig. Corrugation Process

It has 3 rolls & 1hp motor & gum pot. Rotate with high speed about 1000 rpm .then the gum is sticking with a roll. It carry 3 rolls & 1hp motor & gum pot

Technical Data:-

Size Motor Weight Aprox Floor Space

(Inches) (H.P) (Kilo Gram)

55 1/2 500 6'*3'

65 1/2 600 7'*3'

75 1/2 700 8'*3'

85 1/2 800 9'*3'

Precision grinded rolls, the glue is applied to the tips of the corrugated surface of the sheet. The pressure on sheet & control of gum is adjustable from single side. All gears and v belts are covered for safety.

METHOLOGY

MADM MATHOD

MULTI ATTRIBUTE DECISION MAKING (MADM)

MADM methods, on the other hand, are generally discrete, with a limited number of predetermined alternatives.

MADM is an approach employed to solve problems involving selection from among a finite number of alternatives.

An MADM method specifies how attribute information is to be processed in order to arrive at a choice. MADM methods require both inter- and intra-attribute comparisons, and involve appropriate explicit takeoffs.

PARTS OF MADM METHOD

Each decision table (also called decision matrix) in MADM methods has four main parts, namely:

(a) Alternatives,

(b) Attributes,

(c) Weight or relative importance of each attribute

(d) Measures of performance of alternatives with respect to the attributes.

Given the decision table information and a decision-making method, the task of the decision maker is to find the best alternative and/or to rank the entire set of alternatives.

It may be added here that all the elements in the decision table must be normalized to the same units, so that all possible attributes in the decision problem can be considered.

Decision table in MADM methods

The decision table shows

Alternatives, Ai (for i = 1, 2, ….. , N),

Attributes, Bj (for j = 1, 2, ….. , M),

Weights of attributes, wj (for j=1, 2, ….., M) and

The measures of performance of alternatives, mij (for i= 1, 2, ….., N; j=1, 2, ….., M).

SELECTION OF AN ATTRIBUTE

Table:- 1 shows attributes and their alternatives

APPLIED METHODS

1]Analytic Hieryachi Process (Ahp):

2]Technique for Order Preference by Similarity to Ideal Solution (TOPSIS) Method:

3]Preference Ranking Organisation Method For Enrichment And Evaluation   (PROMETHEE)

CALCULATIONS

| Preference scale | Numerical value |
| --- | --- |
| Very strong | 1 |
| Strong importance | 2 |
| Absolute strong | 3 |
| Between strong &very strong | 4 |
| Between strong &absolute strong | 5 |

Table:- 2 Information regarding the Attribute is as follows

Table:-3 Relative Importance is as follows

1] CALCULATIONS FOR AHP METHOD

TABLE:- 4  Pair Wise Comparison Matrix

TABLE:- 5  Weights of Attributes

Table:-6  Decision Matrix Table

Table:-7   Composite Performance Score

| Industry | Consistency Index | Score |
| --- | --- | --- |
| 1 | 3.413-2/3 | o.471 |
| 2 | 4.306-2/3 | 0.768 |
| 3 | 4.786-2/3 | 0.928 |

Table:-8 Ranking of an Industry By AHP method

|  | Industry Ranking |
| --- | --- |
| Industry 3 | 0.928 |
| Industry 2 | 0.768 |
| Industry 1 | 0.471 |

Table:-9  Ranking of an Industry By TOPSIS Method

| Industry 2 | 0.086 |
| --- | --- |
| Industry 3 | 0.21 |
| Industry 1 | 0.10 |

Table:-10 Ranking of Industry By PROMETHREE Method

| Industry2 | 0.731 |
| --- | --- |
| Industry3 | 0.721 |
| Industry1 | -0.98 |

RESULT AND CONCLUSION

[1] From these three result of ranking table in calculation we can say that …

Industry2 >  Industry 3 > Industry1  and CR of Industry 2 is more close to 1 than other two industries ,therefore Industry 2 is best .

[2] By using one of the MADM method like AHP and PROMETHREE, we can find out best optimal solution by comparing the values of each of industry.

[3] With this analysis we  can find out  which MADM is more effective for different set of problem. So here , two techniques such as AHP and PROMETHREE are more effective than TOPSIS.

REFERENCES

[1](Cheng-Fang Hong1 Hui-Ling Chang)Journal of  Quality Vol. 15, No. 2(2008))Multiple Attributes Decision-Making Model for Medical Service Selection

[2](Yashuai LI2 construction research 2012)Multi-Attribute Decision Making in Choosing Suitable Construction Waste Management Methods

[3] (Devi, S. P. Yadav, and S. Kumar,Vol. 7, 2009, pp. 58-62. 9. S. K. Cheng,) “Extension of fuzzy TOPSIS method based on vague sets,” Computational Cognition

[4] (Canada, 2000. 10. C. Yeh,)“Development of a fuzzy multi-criteria decision support system for municipal solid waste management,” Master Thesis, Applied Science in Advanced Manufacturing and Production Systems, University of Regina,

[5](Research, Vol. 9, 2002, pp. 169-181. 11. H. Soltanpanah, H. Farughi, and M. Golabi,)“A problem-based selection of multi-attribute decision making methods,” International Transactions in Operational

[6](Issue 60, 2010, pp. 175-188. 12. E. Triantaphyllou,)“Utilization and comparison of multi attribute decision techniques to rank countries upon human development rate,” International Research Journal of Finance and Economics

[7]Multi-attribute Decision Making Methods: A Comparative Study, Kluwer Academic Publishers, Boston, 2000. 13. J. Lezzi, “Multi-criteria decision making in outpatient scheduling,” Master Thesis

[8](Springer Verlag, NY, 1981. 16.K. Yoon and C. L. Hwang,) Multiple Attribute Decision Making Methods and Applications,