EFFECT OF DIAPHRAGM FLEXIBILITY ON THE SEISMIC RESPONSE OF RCC FRAMED BUILDING CONSIDERING DIAPHRAGM DISCONTINUITY

Akshay Nagpure1, S. S. Sanghai2

1PG Student, Department of Civil Engineering, G.H. Raisoni College of Engineering, Nagpur

2Assistant Professor, Department of Civil Engineering, G.H. Raisoni College of Engineering, Nagpur

1 akshaynagpure7@gmail.com, 2 sanket.sanghai@raisoni.net

Abstract - Diaphragms are required to be designed as part of the seismic force-resisting system of every new building as they distribute lateral forces to the vertical elements of lateral force resisting system. Concrete diaphragms consist of different element which plays an important role in resisting lateral loads. Diaphragms acts differently according to the configurations of the building and type of load acting on it. In a RCC framed building, different columns may carry different loads accordingly. In this paper, RCC framed building structures have been analyzed using ETABS software by linear time history analysis by changing flexibility of the floors and simultaneously when plan irregularities are provided. Time history record of El Centro Earthquake has been provided to the software.   Responses of all those structures has been plotted and discussed. An attempt is made in this paper to compare the responses of  the structures  when floor diaphragm flexibility is changed and simultaneously plan irregularities are provided.

Keywords: Floor Diaphragm, Stiffness, Earthquake, Flexible Diaphragm, Rigid Diaphragm, Reinforced Concrete, Shear Wall

- Introduction

A multi-storied framed building can have various types of irregularities and that can affect the normal response of the building. Here we are considering the plan irregularity i.e. diaphragm discontinuity. Diaphragm with abrupt discontinuities or change in stiffness can also affect the normal responses. Along with the diaphragm discontinuity, the variation with flexibility of the slab can be compared to know the variation in responses when discontinuities of same area were placed at different places.

As per IS 1893 (Part 1) 2016, a diaphragm may be classified into following two types,

- Flexible Floor Diaphragm - As per IS 1893, a floor diaphragm whose maximum lateral displacement measured from the chord of deformed shape at any point of the diaphragm exceeds 1.2 times the average displacement of entire diaphragm is  known as Flexible floor Diaphragm.

- Rigid Floor Diaphragms - A floor diaphragm whose maximum lateral displacement measured from the chord of deformed shape at any point of the diaphragm does not exceed 1.2 times the average displacement of entire diaphragm is considered to be Rigid Floor diaphragm. Rigid diaphragm distributes the horizontal forces to the vertical resisting elements in direct proportion to the relative rigidities. It is based on the assumption that the diaphragm does not deform itself and will cause each vertical element to deflect the same amount. This may be determined by comparing the computed midpoint in-plane deflection of the diaphragm itself under lateral load with the drift to adjoining vertical elements under tributary lateral load.

Fig 1 - Flexible Floor Diaphragm

2.0 Objectives

- To compare the effect of diaphragm flexibility of the building on the responses under seismic load.

- To compare the responses the building structure when the openings are provided at the different places of the plan.

- To study the effect of diaphragm flexibility on the seismic responses of the building when diaphragm discontinuity is considered.

3.0 Geometric details of model

For the study, one model was considered. The geometric details have been shown in Table 1. For the analysis, Time history method was used.

Table 1 Geometric Details

| No of Storeys | G + 16 |
| --- | --- |
| Storey Height | 3 m |
| Number of Bays | 6 bays in both the directions |
| Beam Size | 350 mm x 900 mm |
| Column Size | 350 mm x 1100 mm |
| Grade of Concrete | M30 |
| Grade of Steel | Fe415 |
| Slab Thickness | 110 mm |
| Seismic zone type | Zone II |
| Method of analysis | Time History analysis |
| Ground motion data | Time History record of El Centro Earthquake |

4.0 Modeling of flexible Floor Diaphragm

Computer software ETABS were used to model flexible floor Diaphragm. The software consist of a tool STIFFNESS MODIFIERS which is used to make the slab flexible shown in the figure.

`

Fig 2 - Stiffness Modifier Tool

Fig 3 - Shell Element Forces

The membrane forces are the in plane forces in respective directions whereas Bending moments are plate bending or twisting moments as shown in the figure. The stiffness of the floors were modified by considering all these parameters. Diaphragms with all these parameters 1 acts as a rigid floor diaphragm. The stiffness of the slab can be reduced by certain percentage out of 1.The analysis is done using linear time history analysis considering ground motion record of El Centro Earthquake.

5.0 Building with Diaphragm discontinuity

Discontinuity is provided by providing openings to the floors of equal area at different places of the floor.Percentage of Opening provided is 11.11 % .The following patterns were provided and responses were studied.

(a)  Opening at the Centre                                                                (b) Opening at the Corners

(c) Opening at the Horizontal faces                                                       (d) Openings at the Vertical Faces

Fig 4 -  Buildings with diaphragm discontinuity

6.0 Results and Discussion

6.1 Base Shear Comparison

When Stiffness of Load resisting system reducing, base shear of the structure is also reducing.

Fig 5 – Base Shear Comparison

In X direction, base shear has reduced with the reduction in stiffness of slab but does not gave considerable difference in while changing the place of opening on the slab. In Ydirection also, the base shear went on reducing with increase in flexibility of the slab with very less difference with the change in the places of the opening.

6.2 Column Forces

6.2.1 Column Axial Force

Reduction in the stiffness of the floor leads to reduction  in the column axial forces in the stiffer direction.

Fig 6 – Column Axial Force comparison for all load cases

Axial Force is reducing as per reducing stiffness in X direction. Opening provided at the centre of the plan produced  the largest axial force. In Y direction, axial force increased as per reducing stiffness of the slab and openings when given at the vertical sides produces largest axial force as compared to all other models but model with opening at the horizontal faces has given much smaller value of axial force.

6.2.2  Maximum Column Shear Force Comparison

Fig 7 – Column Shear Force comparison for all load cases

In X direction, column shear force goes on reducing while reducing the stiffness of the slab and plan with opening at the centre produces largest shear force. In Y direction, Shear force goes on increasing but plan with opening at the horizontal faces has given much lesser shear force.

6.2.3 Maximum Bending Moment

Fig 8 – Column Bending Moment comparison for all load cases

Maximum Bending Moment of Column has decreased with the decrease in stiffness of the floors in X direction.In Y direction, Maximum Bending Moment of Column has increased with the decrease in stiffness of the floors.

6.3 Beam Forces

6.3.1 Beam Axial Forces

As the Stiffness of the floor reduces, beam forces goes on increasing because beams starts carrying forcesin places of Floors. Beams acts as a collectorsin the building structure.

Beam axial force increases with decrease in stiffness of the slab and maximum. Beam axial force is produced by the structure having plan opening at the corners.

Fig 9 – Beam Axial Force comparison for all load cases

Beam axial force has increased with decrease in stiffness of the slab in both the directions.

6.3.2  Shear Force Comparison

Fig 10 – Beam Shear Force comparison for all load cases

Shear Force in X direction is decreasing with decrease in stiffness of the slab whereas it is increasing as per reducing stiffness of floors.

6.3.3 Maximum Bending Moment Comparison

Fig 11 – Beam Bending Moment comparison for all load cases

Bending moment is increasing with the reduction in stiffness of thr floors in both the directions. Structure with plan opening at the centre gives much less Bending moment in X direction. Slab opening when provided at the corners gives maximum response of Bending Moment.

6.4 Time Period Comparison

Fig 12 – Time Period Comparison for all Load Cases

Time period does does not show any variation with the placing of openings in different places. But as per decreasing stiffness, time period has increased.

6.5 Maximum Storey Displacement

6.5.1 For Plan with opening at the centre

| Storey | Storey Displacement(mm) for Stiffness Percentage |
| --- | --- |
|  | 100% | 75% | 50% | 25% |
| Story16 | 23.883 | 23.827 | 23.771 | 23.712 |
| Story15 | 23.39 | 23.321 | 23.258 | 23.192 |
| Story14 | 22.709 | 22.642 | 22.568 | 22.497 |
| Story13 | 21.788 | 21.722 | 21.65 | 21.572 |
| Story12 | 20.631 | 20.567 | 20.498 | 20.422 |
| Story11 | 19.273 | 19.201 | 19.125 | 19.053 |
| Story10 | 17.738 | 17.672 | 17.6 | 17.522 |
| Story9 | 16.055 | 15.987 | 15.913 | 15.839 |
| Story8 | 14.263 | 14.203 | 14.139 | 14.07 |
| Story7 | 12.405 | 12.348 | 12.288 | 12.225 |
| Story6 | 10.495 | 10.445 | 10.392 | 10.337 |
| Story5 | 8.561 | 8.518 | 8.476 | 8.432 |
| Story4 | 6.62 | 6.588 | 6.554 | 6.519 |
| Story3 | 4.682 | 4.658 | 4.632 | 4.606 |
| Story2 | 2.777 | 2.761 | 2.745 | 2.728 |
| Story1 | 1.036 | 1.03 | 1.024 | 1.018 |
| Base | 0 | 0 | 0 | 0 |

In X Direction		                         In Y Direction

| Storey | Storey Displacement(mm) for Stiffness Percentage |
| --- | --- |
|  | 100% | 75% | 50% | 25% |
| Story16 | 25.609 | 25.643 | 25.681 | 25.724 |
| Story15 | 25.295 | 25.326 | 25.359 | 25.396 |
| Story14 | 24.848 | 24.88 | 24.915 | 24.954 |
| Story13 | 24.247 | 24.281 | 24.317 | 24.357 |
| Story12 | 23.504 | 23.539 | 23.577 | 23.618 |
| Story11 | 22.608 | 22.644 | 22.682 | 22.724 |
| Story10 | 21.516 | 21.551 | 21.589 | 21.63 |
| Story9 | 20.179 | 20.212 | 20.247 | 20.286 |
| Story8 | 18.587 | 18.618 | 18.653 | 18.692 |
| Story7 | 16.771 | 16.799 | 16.83 | 16.864 |
| Story6 | 14.766 | 14.788 | 14.814 | 14.843 |
| Story5 | 12.583 | 12.602 | 12.622 | 12.644 |
| Story4 | 10.216 | 10.231 | 10.248 | 10.267 |
| Story3 | 7.692 | 7.704 | 7.717 | 7.732 |
| Story2 | 5.052 | 5.06 | 5.068 | 5.077 |
| Story1 | 2.351 | 2.354 | 2.358 | 2.362 |
| Base | 0 | 0 | 0 | 0 |

6.5.2 For Plan with opening at the Corners

In X direction                                                                                          In Y direction

| Storey | Storey Displacement(mm) for Stiffness Percentage |
| --- | --- |
|  | 100% | 75% | 50% | 25% |
| Story16 | 25.611 | 25.644 | 25.679 | 25.721 |
| Story15 | 25.296 | 25.327 | 25.361 | 25.398 |
| Story14 | 24.85 | 24.882 | 24.917 | 24.955 |
| Story13 | 24.251 | 24.284 | 24.319 | 24.359 |
| Story12 | 23.509 | 23.543 | 23.58 | 23.622 |
| Story11 | 22.614 | 22.649 | 22.687 | 22.731 |
| Story10 | 21.523 | 21.557 | 21.594 | 21.637 |
| Story9 | 20.186 | 20.218 | 20.253 | 20.294 |
| Story8 | 18.594 | 18.625 | 18.659 | 18.7 |
| Story7 | 16.777 | 16.805 | 16.836 | 16.871 |
| Story6 | 14.772 | 14.794 | 14.82 | 14.85 |
| Story5 | 12.589 | 12.607 | 12.627 | 12.651 |
| Story4 | 10.221 | 10.236 | 10.253 | 10.273 |
| Story3 | 7.696 | 7.708 | 7.721 | 7.736 |
| Story2 | 5.055 | 5.062 | 5.07 | 5.079 |
| Story1 | 2.352 | 2.355 | 2.359 | 2.364 |
| Base | 0 | 0 | 0 | 0 |

| Storey | Storey Displacement(mm) for Stiffness Percentage |
| --- | --- |
|  | 100% | 75% | 50% | 25% |
| Story16 | 23.9 | 23.837 | 23.774 | 23.716 |
| Story15 | 23.398 | 23.328 | 23.265 | 23.199 |
| Story14 | 22.718 | 22.65 | 22.575 | 22.505 |
| Story13 | 21.798 | 21.731 | 21.658 | 21.58 |
| Story12 | 20.641 | 20.576 | 20.506 | 20.43 |
| Story11 | 19.285 | 19.211 | 19.133 | 19.061 |
| Story10 | 17.75 | 17.682 | 17.608 | 17.529 |
| Story9 | 16.068 | 15.997 | 15.922 | 15.846 |
| Story8 | 14.275 | 14.212 | 14.146 | 14.076 |
| Story7 | 12.416 | 12.357 | 12.295 | 12.23 |
| Story6 | 10.506 | 10.454 | 10.399 | 10.341 |
| Story5 | 8.57 | 8.526 | 8.481 | 8.436 |
| Story4 | 6.627 | 6.594 | 6.558 | 6.522 |
| Story3 | 4.688 | 4.662 | 4.636 | 4.608 |
| Story2 | 2.781 | 2.765 | 2.747 | 2.73 |
| Story1 | 1.037 | 1.031 | 1.025 | 1.018 |
| Base | 0 | 0 | 0 | 0 |

6.5.3 For Plan with opening at the Horizontal Faces

In X direction							In Y direction

| Storey | Storey Displacement(mm) for Stiffness Percentage |
| --- | --- |
|  | 100% | 75% | 50% | 25% |
| Story16 | 25.724 | 25.682 | 25.645 | 25.612 |
| Story15 | 25.396 | 25.36 | 25.327 | 25.297 |
| Story14 | 24.954 | 24.916 | 24.882 | 24.85 |
| Story13 | 24.357 | 24.318 | 24.283 | 24.25 |
| Story12 | 23.618 | 23.578 | 23.542 | 23.508 |
| Story11 | 22.724 | 22.684 | 22.647 | 22.613 |
| Story10 | 21.63 | 21.59 | 21.554 | 21.52 |
| Story9 | 20.286 | 20.249 | 20.215 | 20.184 |
| Story8 | 18.692 | 18.655 | 18.622 | 18.592 |
| Story7 | 16.864 | 16.832 | 16.803 | 16.775 |
| Story6 | 14.843 | 14.816 | 14.791 | 14.77 |
| Story5 | 12.644 | 12.623 | 12.604 | 12.587 |
| Story4 | 10.267 | 10.249 | 10.234 | 10.219 |
| Story3 | 7.731 | 7.718 | 7.706 | 7.695 |
| Story2 | 5.077 | 5.068 | 5.061 | 5.054 |
| Story1 | 2.362 | 2.358 | 2.355 | 2.352 |
| Base | 0 | 0 | 0 | 0 |

| Storey | Storey Displacement(mm) for Stiffness Percentage |
| --- | --- |
|  | 100% | 75% | 50% | 25% |
| Story16 | 23.882 | 23.826 | 23.771 | 23.716 |
| Story15 | 23.392 | 23.323 | 23.263 | 23.198 |
| Story14 | 22.711 | 22.644 | 22.571 | 22.504 |
| Story13 | 21.79 | 21.724 | 21.653 | 21.577 |
| Story12 | 20.632 | 20.569 | 20.501 | 20.427 |
| Story11 | 19.274 | 19.202 | 19.128 | 19.058 |
| Story10 | 17.739 | 17.673 | 17.602 | 17.526 |
| Story9 | 16.056 | 15.988 | 15.915 | 15.843 |
| Story8 | 14.264 | 14.204 | 14.14 | 14.073 |
| Story7 | 12.405 | 12.349 | 12.289 | 12.227 |
| Story6 | 10.496 | 10.446 | 10.393 | 10.339 |
| Story5 | 8.561 | 8.518 | 8.476 | 8.434 |
| Story4 | 6.62 | 6.588 | 6.554 | 6.52 |
| Story3 | 4.682 | 4.658 | 4.633 | 4.607 |
| Story2 | 2.777 | 2.761 | 2.745 | 2.729 |
| Story1 | 1.037 | 1.031 | 1.024 | 1.018 |
| Base | 0 | 0 | 0 | 0 |

6.5.4 For Plan with opening at the Horizontal Faces

In X Direction         				In Y Direction

| Storey | Storey Displacement(mm) for Stiffness Percentage |
| --- | --- |
|  | 100% | 75% | 50% | 25% |
| Story16 | 23.893 | 23.832 | 23.774 | 23.711 |
| Story15 | 23.397 | 23.326 | 23.262 | 23.195 |
| Story14 | 22.716 | 22.647 | 22.572 | 22.499 |
| Story13 | 21.797 | 21.729 | 21.655 | 21.575 |
| Story12 | 20.64 | 20.575 | 20.503 | 20.426 |
| Story11 | 19.283 | 19.209 | 19.131 | 19.057 |
| Story10 | 17.749 | 17.68 | 17.606 | 17.526 |
| Story9 | 16.067 | 15.996 | 15.92 | 15.843 |
| Story8 | 14.274 | 14.212 | 14.144 | 14.073 |
| Story7 | 12.416 | 12.357 | 12.294 | 12.227 |
| Story6 | 10.506 | 10.453 | 10.397 | 10.339 |
| Story5 | 8.57 | 8.525 | 8.48 | 8.434 |
| Story4 | 6.627 | 6.593 | 6.558 | 6.52 |
| Story3 | 4.687 | 4.662 | 4.635 | 4.607 |
| Story2 | 2.781 | 2.764 | 2.747 | 2.729 |
| Story1 | 1.037 | 1.031 | 1.025 | 1.018 |
| Base | 0 | 0 | 0 | 0 |

| Storey | Storey Displacement(mm) for Stiffness Percentage |
| --- | --- |
|  | 100% | 75% | 50% | 25% |
| Story16 | 25.608 | 25.639 | 25.721 | 25.721 |
| Story15 | 25.295 | 25.326 | 25.398 | 25.398 |
| Story14 | 24.849 | 24.881 | 24.955 | 24.955 |
| Story13 | 24.248 | 24.282 | 24.359 | 24.359 |
| Story12 | 23.506 | 23.541 | 23.622 | 23.622 |
| Story11 | 22.611 | 22.647 | 22.731 | 22.731 |
| Story10 | 21.519 | 21.554 | 21.638 | 21.638 |
| Story9 | 20.182 | 20.216 | 20.295 | 20.295 |
| Story8 | 18.59 | 18.622 | 18.701 | 18.701 |
| Story7 | 16.773 | 16.803 | 16.872 | 16.872 |
| Story6 | 14.769 | 14.792 | 14.851 | 14.851 |
| Story5 | 12.585 | 12.605 | 12.652 | 12.652 |
| Story4 | 10.218 | 10.234 | 10.274 | 10.274 |
| Story3 | 7.694 | 7.706 | 7.737 | 7.737 |
| Story2 | 5.053 | 5.061 | 5.08 | 5.08 |
| Story1 | 2.351 | 2.355 | 2.364 | 2.364 |
| Base | 0 | 0 | 0 | 0 |

There is no any considerable difference found in the storey drift .

7.0 Concluding Remarks

On studying the above literatures, we have reached to the following conclusions,

- Floor Diaphragm Flexibility affects Base Shear of the Building, Column Forces, Beam Forces but doesn’t show considerable difference in Time Period and Storey Drift.

- Orientation of the openings in the building plan changes the responses of the structure under seismic load.

- The Flexibility of the slabs plays vital role in reducing Base Shear, Column Axial Forces.

- Base shear and Column axial force has been reduced as per increasing flexibility of the floors when THA is applied in X direction but reduction has been found when THA is applied in Y Direction.

- Opening at the faces of the floors in shorter side gives comparatively larger Base Shear but Column forces where found higher when openings were in longer side.

References

- Eivani, Hamed, et al. "Seismic Response of Plan-Asymmetric Structures with Diaphragm Flexibility." Shock and Vibration2018 (2018).

- Kollerathu, Jacob A., and Arun Menon. "Role of diaphragm flexibility modeling in seismic analysis of existing masonry structures." Structures. Vol. 11. Elsevier, 2017.

- IS1893, B. I. S. "Indian Standard criteria for earthquake resistant design of structures (part 1): general provisions and buildings (sixth revision, Bureau of Indian Standards, New Delhi." Google Scholar (2016).

- Soeprapto, Gambiro, et al. "Effect of longitudinal joint on the shear-key of hollow core slab which function as an rigid diaphragm." MATEC Web of Conferences. Vol. 101. EDP Sciences, 2017.

- Zahrai, S. M., and L. Sarkissian. "IN-PLANE RIGIDITY OF LATERALLY LOADED COMPOSITE FLOOR SYSTEMS, A FINITE ELEMENT APPROACH." (2015): 161-181.

- Scarry, J. M. "Floor diaphragms–Seismic bulwark or Achilles’ heel." New Zealand Society for Earthquake Engineering Conference. 2014.

- Bhuiyan, Mohammad T., and Roberto T. Leon. "Effect of diaphragm flexibility on tall building responses." Structures Congress 2013: Bridging Your Passion with Your Profession. 2013.

- Lawson, J. W., and C. N. Yarber. "Collective chord behavior in large flexible diaphragms." Structures Congress 2013: Bridging Your Passion with Your Profession. 2013.

- Fouad, Kehila, Zerzour Ali, and Remki Mustapha. "Structural Analyses With Flexibility Effect Of The Floor Slabs." Proceedings of the Fifteenth World Conference of Earthquake Engineering, Lisboa, Portugal. 2012.

- Moehle, Jack P., et al. "Seismic design of cast-in-place concrete diaphragms, chords, and collectors." Seismic design technical brief, US Department of Commerce, Building and Fire Research Laboratory, National Institute of Standards and Technology (2010).