Seismic analysis of concentric bracing in high rise steel structure

Mr. Nikhil Shingade1, Mr. Nikhil Pitale2

- PG Student, Department of Civil Engineering, G. H. Raisoni college of engineering, Nagpur

- Assistant Professor, Department of Civil Engineering, G.H. Raisoni college of engineering, Nagpur

---------------------------------------------------------------------***---------------------------------------------------------------------

Abstract – Now a days steel bracing are major and important part of the RCC as well as steel Structure. In any high rise structure to reduce displacement and modal time bracing are use. It play imp role to make structure  stable from wind force and seismic force. In this present study concentric bracing are use on high rise steel structure and seismic  effect of bracing system is studied  using IS 1893:2016. Seismic analysis has been conducted to evaluate the effect of different bracing at different arrangement in high rise steel structure. Analysis is carried on X bracing, diagonal bracing, inverted V bracing and V bracing For this study G+15 high rise steel structure is mode  by using IS 800:2007on ETABS 2016. Seismic zone is III and soil is medium soil with response reduction factor is 5

Keywords: Concentric bracing, high rise steel structure, response spectre method, displacement, base shear.

INTRODUCTION

Recently all over the world steel are commonly use in construction. For any high rise steel structure steel are commonly used as a structural material. Steel are more stable than RCC. Steel bracing are use to make structure more stiffed. Steel bracing reduce displacement and modal time of structure and also help to reduce story drift. Generally steel bracing improve base shear of structure. Stability of structure can be increases by using steel bracing against wind and earthquake. Bracing can be apply on bridge transmissions towers etc. it is easy to construed and it is in bolted in connection.

There are two types of bracing

1) Concentric bracing  2) Eccentric bracing

Concentric bracing are that bracing which intersect at node and the centroid of member is passes through the same point. Concentric bracing are easy to construct and reduce strory displacement  and model time period. Concentric bracing in stability of structure

Eccentric bracing are that bracing which are depend on link that are created through eccentricity with either beam or column. It also reduce displacement and model time period.

DETAILS OF THE STRUCTURE

- Modeling and analysis

High rise steel structure of G+15 are  modeled on ETABS. Analysis is carried out on ETABS software. Different type of bracing systems for building are modeled and analysis for seismic load. The plan dimension of the building is 16m X 24m and height of story is 3m

- Properties of building

No of stories 	:	G+15

Beam 		:	ISMB 300

Column		:	ISMB 600

Bracing		:	150X150X15

- Loading details

Floor load and members weight and calculated as per general consideration as per IS 875 Part I. live load is 4 KN/N as per IS 875 Part II

- Seismic loading

Seismic load is given as per IS 1893:2016 Part II

Zone		:	3

Zone Factor	:	0.16

Soil type		 :	Medium

Fig 1: Plan of Study Work

Fig2: Elevation of G+15

RESULT

- Model time Period

1.1 Comparison between model period (second) of bracing at different location

Fig9: Structural of model time Period in second

1.2 Comparison between decrease of model period (% reduction) of bracing at different  location in seconds

Fig10: Structural of model time Period  in percentage

- Displacement

2.1 Comparison between  displacement(mm) of bracing at different location in X direction

Fig11: G+15 Displacements (mm) in X direction

2.2 Comparison between decrease of displacement(% reduction) of bracing at different  location in X direction

Fig12:  G+15 Displacements (%) in X direction

2.3 Comparison between displacement(mm) of bracing at different location in Y direction

Fig13: G+15 Displacements (mm) in Y direction

2.4 Comparison between decrease of displacement (%reduction) of bracing at different location in Y direction

Fig14: G+15 Displacements (%) in Y direction

- Base shear

3.1 Comparison  of base shear(KN) when bracing is applied at different location in X direction

Fig15:  G+15 Base Shear (KN) in X direction

3.2 Comparison  of percentage in increases in base shear(KN) when bracing is applied at different location in X direction

Fig16: G+15 Base Shear (%) in X direction

3.3 Comparison  of base shear(KN) when bracing is applied at different location in Y direction

Fig17: G+15 Base Shear (KN) in Y direction

3.4 Comparison  of percentage in increases in base shear(KN) when bracing is applied at different location in Y direction

Fig 18 G+15 Base Shear (%) in Y direction

CONCLUSION

The following are the observations from the present analysis.

1.Steel framed structure with concentric X bracing are possessing higher ductility reduction higher strength against seismic force when compared to unbraced, v bracing inverted and diagonal bracing.

2. Cross pattern arragement are improving base shear and reducing displacement and model time period as compare to corner and center arrangement.

3. X barcing are improving base shear and reducing displacement in compare of diagonal bracing, inverted V bracing and V bracing.

4. Overall concentric X bracing giving better result for seismic analysis.

5. By considering lateral stiffness, the concentric X bracing has been found the most suitable one for steel building studied under the present study.

REFERENCES

[1]Sangle, K. K., K. M. Bajoria, and V. Mhalungkar. lisboa, “Seismic analysis of high rise steel frame building with and without bracing with and without bracing." 2012.

[2] Mohammad EyniKangavar “Seismic Propensity of Knee Braced Frame (KBF) As Weighed Against Concentric Braced Frame (CBF) Utilizing ETABS and OPENSEES” in International Journal of Engineering and Advanced Technology (IJEAT) ISSN: 2249 – 8958, Volume-5 June-2012 Pp no 141152.

[3] M.D. Kevadkar, P.B. Kodag“lateral load analysis of RCC building”,(2013),

[4]Sudharani,M., and G.Nandini Devi. " Seismic Demand of Steel Structural Systems" IJAIEM Volume 5, Issue 3, March, 2016

[5] Martin, Geoffrey R., and Ignatius Po Lam. "Earthquake resistant design of foundations-retrofit of existing foundations." ISRM International Symposium. International Society for Rock Mechanics, 2000.

[6]Tafheem Z. and  Khusru S., “Structural behavior of steel building with concentric and eccentric bracing: A comparative study”, International Journal of Civil and Structural Engineering, vol 4, No 1, 2013, pp 12-19.

[7]Khan M. I. and Khan K.N.,(2014), “Seismic Analysis of Steel Frame with Bracings using Pushover Analysis”, International Journal of Advanced Technology in Engineering and Science, Volume No. 02, Issue No. 07, Page No. 369-381.

[8]Luigi Di Sarno and Amr S. Elnashai, “Bracing system for seismic retrofitting of steel frames”, 13th World Conference on Earthquake Engineering, Vancouver, International Journal of Scientific Research Engineering, 2014,vol11

[9]jagadish j.s, tejas d. Doshi,“A Study on Bracing Systems on High Rise Steel Structures”, International Journal of Engineering Research and Technology, Volume 2, July 2013.

[10]Martino, R., E. Spacone, and G. Kingsley. "Nonlinear pushover analysis of RC structures." Advanced technology in structural engineering .ASCE 2000. 1-8.

[11] Huang, Wei, and Phillip L. Gould. "3-D pushover analysis of a collapsed reinforced concrete chimney." Finite elements in analysis and design 43.11-12 (2007): 879-887.

[12] Maheri, M. R., and A. Sahebi. "Use of steel bracing in reinforced concrete frames." Engineering Structures 19.12 (1997): 1018-1024.

# Text boxes

Corner X bracing

Corner diagonal bracing

Corner V bracing

Corner inverted V bracing

Center X bracing

Center diagonal bracing

Center V bracing

Center inverted V bracing

Cross pattern X bracing

Cross pattern  diagonal  bracing

Cross pattern inverted V bracing

Cross pattern  V bracing